Outlook
Overview
CMS Karlsruhe:
1) Study of W → μ ν, Z → μ μ and W Mass MW
  1. (V.Buege, C. Jung, G. Quast, A. Schmidt)
2) High pT Jet Cross Sections
  1. (A. Oehler, K. Rabbertz)
DESY, Fermilab, Uni Karlsruhe:
3) fastNLO: Fast repeated Jet σ Calculation
(T. Kluge, M. Wobisch, K. Rabbertz)

---
Study of W → μ ν, Z → μ μ
-Transverse mass method for MWvery sens. to exp. uncertainties
- High Z statistic available at LHC
→ Use similar properties of W and Z decays (Giele, Keller, 1998)
Idea:
- Compare mT distributions of W and „morphed Z“ (reduction of Z mass to W test mass, consider one muon as a neutrino, ...)
- Extract W mass from Chi2 fit
- Study of cancellation of syst, uncertainties ongoing (μ resol., acceptance, B field, ...)
- Needs a lot of statistics (O(10M) events) for 1 fb-1 => use fast simulation
Fit range
ΔMW:3.4 ± 39.0 MeV
Lint = 1 fb-1

---
High pT Jet Cross Sections
- Measurable right from the start
- Tests detector performance
- Checks SM extrapolation to LHC
energies!
Stat. uncertainties after 1 fb-1
Lint = 1 fb-1
- Important exp. ingredient: Jet energy calibration
- Theory: NLO calculation (NLOJET++, Z. Nagy and
fastNLO, see next page)
- Allows fitting of the strong coupling and the pdfs
Hard Partons
Partonic Final State
Hadronic Final State
PYTHIA / HERWIG
Uncalibrated Jets
Calorimeter Jets
NLO Calculation
Corrected Jets
   PARTON SHOWER
  HADRONIZATION, DECAYS
JET CALIBRATION
RECONSTRUCTION
ORCA
   MC CORRECTIONS

---
fastNLO
Repeating theory calculations (pdfs, αS, μR, μF) for comparison with data very time consuming
fastNLO extracts necessary data into one table
One long calculation first, repetition with e.g. other pdf takes only seconds!
Table writing has to be implemented for every observable
Working examples with interactive web interface exist on fastNLO project page at CEDARhttp://hepforge.cedar.ac.uk/fastnlo

---
Discussion Topics
Other interesting quantities/analyses to perform, especially at start up?
Experience comparing PYTHIA, HERWIG, ... at LHC energies? Other MCs? Parameter tuning?
Experience comparing with MC@NLO at LHC energies?