Title
 Jets and αs
Experimental status
Klaus Rabbertz, KIT
(on behalf of ATLAS & CMS)

---
Outline
2012: No LHC results yet
PDG2012
- Motivation
- Jet-like measurements
  - Cross sections
  - Ratios
  - Normalised distributions
- Issues & perspectives
- Summary & outlook

---
Jets at the LHC
Abundant production of jets:
Jets at hadron colliders provide the highest reach ever to determine the strong coupling constant at high scales Q
Also learn about hard QCD, the proton structure, non-perturbative effects,
    and electroweak effects at high Q
Proton Structure
(PDF)
Proton Structure
(PDF)
Matrix Element
Hadrons

---
Jets at the LHC
Abundant production of jets:
Extract αs(MZ), the least precisely known fundamental constant!
Proton Structure
(PDF)
Proton Structure
(PDF)
Matrix Element
Hadrons

---
Jets at the LHC
Adapted from Pietro Govoni yesterday ...

---
Jet cross sections ~ αs2
- Determination of αs(MZ) in single-parameter fit
- Test consistency of running of αs(Q)
- Multi-parameter fit of αs(MZ) & PDFs

---
All inclusive
ATLAS:
EPJC 73 (2013) 2509; JHEP 02 (2015) 153; JHEP 09 (2017) 020; JHEP 05 (2018) 195.
CMS:
PRD 87 (2013) 112002; PRD 90 (2014) 072006; EPJC 75 (2015) 288;
EPJC 76 (2016) 265; EPJC 76 (2016) 451; JHEP 03 (2017) 156.
Relevant ATLAS & CMS measurements:
Proton
Proton
Large transverse momenta
Every jet counts

---
Inclusive jets: cross section
Overall agreement with predictions of QCD at NLO
over many orders of magnitude in cross section and
even beyond 2 TeV in jet pT and for rapidities |y| up to 3 ~ 5
at √s = 2.76, 7, 8, and 13 TeV.
Here: anti-kt, R=0.4, 13 TeV
Data vs. NLO pQCD x non-pert. x EW corrections
Exp. uncertainties for |y| < 0.5
NLO: Ellis, Kunszt, Soper, PRL 69 (1992) 1496;
        Giele, Glover, Kosower, NPB 403 (1993) 633;
        Z. Nagy, PRD 68 (2003) 094002.

---
Inclusive jets: theory corrections
anti-kt, R=0.4, 13 TeV, |y| < 0.5
Nonperturbative correction factors:
- estimated from tuned MC event generators
- uncertainty of 5 – 15% at pT = 100 GeV
- strongly dependent on jet size R
- less important at high pT
Electroweak correction factors:
- calculated perturbatively
- uncertainty small
- strongly dependent on jet rapidity y
- very important at high pT
EW:
Dittmaier, Huss, Speckner, JHEP 11 (2012) 095.
Frederix et al., JHEP 04 (2017) 076.

---
Inclusive jets: theory corrections
anti-kt, R=0.4, 13 TeV, |y| < 0.5
Nonperturbative correction factors:
- estimated from tuned MC event generators
- uncertainty of 5 – 15% at pT = 100 GeV
- strongly dependent on jet size R
- less important at high pT
Electroweak correction factors:
- calculated perturbatively
- uncertainty small
- strongly dependent on jet rapidity y
- very important at high pT
EW:
Dittmaier, Huss, Speckner, JHEP 11 (2012) 095.
Frederix et al., JHEP 04 (2017) 076.
ALICE, arXiv:1909.09718.
See also CMS, SMP-19-003.

---
Inclusive jets: NNLO & scale choice
anti-kt, R=0.4, 13 TeV
→Talk by
Joao Pires
yesterday
QCD scale choice: μR = μF = pT,jet
- close to recommended one
QCD scale choice: μR = μF = pT,max
- NOT recommended
NNLO:
Currie et al., PRL 118 (2017) 072002,
Acta Phys. Pol. B48 (2017) 955.

---
Inclusive jets: αs
Χ2 fit of αs(MZ) for all jet pT and |y| bins
- In fit: all exp. + PDF + NP uncertainties
- PDFs: CT10 NLO PDF sets for various αs(MZ)
Sensitivity to αs(MZ) at NLO
- CMS: anti-kt R = 0.7 at √s = 8 TeV
- QCD scale choice: μR = μF = pT,jet
Jets @ NNLO not fully used yet in fits @ LHC → in progress
Results for ep: → Britzger et al., EPJC79 (2019) 845.

---
Inclusive jets: αs & PDFs
Simultaneous fit of αs & PDFs possible combining HERA DIS & CMS jet data using xFitter Tool
Reduced uncertainties of gluon PDF
CMS results for αs(MZ) at NLO
Orange shading: external PDF sets
Bluish shading: PDF fit incl. HERA data
√s / [TeV]	lum / [fb-1]	αs(MZ)	exp NP PDF	scale
7	5.0	0.1185	35	+53-24
8	19.7	0.1164	+29-33	+53-28
7	5.0	0.1192	+23-19	+24-39
8	19.7	0.1185	+19-26	+22-18
13 (7 TeV) / 18 (8 TeV) parameter fit
Question: How to deal with uncertainty of
Missing higher orders (aka scale uncertainty)
in PDF fits?
xFitter (HERAFitter): Alekhin et al., EPJC 75 (2015) 304.
First progress → e.g. NNPDF, EPJC79 (2019) 931.

---
Dijets
ATLAS:
JHEP 05 (2014) 059; JHEP 05 (2018) 195.
CMS:
PRD 87 (2013) 112002; EPJC 77 (2017) 746.
Relevant ATLAS & CMS measurements:
Proton
Proton
Large masses

---
Triple-differential dijets
Most measurements done with respect to dijet mass
and either max. rapidity |y|max (CMS) or rapidity separation y* (ATLAS). One CMS result on αs(MZ):
Illustration of dijet event topologies
\frac{d^3\sigma}{dp_\text{T,avg}dy_bdy^*} \propto \alpha_s^2

---
Triple-differential dijets
Simultaneous fit of αs & PDFs combining
HERA DIS & CMS djet data using xFitter Tool
Data over NLO pQCD x non-pert. x EW corrections
Reduced uncertainties of gluon PDF
√s / [TeV]	lum / [fb-1]	αs(MZ)	exp NP PDF	scale
7	5.0	0.1185	35	+53-24
8	19.7	0.1164	+29-33	+53-28
7	5.0	0.1192	+23-19	+24-39
8	19.7	0.1185	+19-26	+22-18
8	19.7	0.1199	+15-16	+31-19
16-parameter fit

---
Multi-jets and αs
ATLAS:
EPJC 75 (2014) 288.
CMS:
EPJC 73 (2013) 2604; EPJC 75 (2015) 186;
PAS-SMP-16-008 (2017).
Relevant ATLAS & CMS measurements:
Higher multiplicity

---
 Cross sections ~ αs3
- As compared to αs2:
  - Higher sensitivity
  - Smaller statistical precision
  - Smaller dynamical range
  - More scale choices
  - Theory at NNLO not available

---
3-jet mass
Sensitive to αs beyond 2→2 process
NLO with 3-4 partons (NLOJet++)
Sensitive to PDFs
Involves additional “scale” pT,3
CMS, EPJC 75 (2015) 186.
μr,μf = m3/2
|y|max = 2.0, pT3 > 100 GeV
Most PDF sets compatible to data
→ αs
Extraction of αS(MZ):
√s / [TeV]	lum / [fb-1]	αs(MZ)	exp NP PDF	scale
7	5.0	0.1171	28	+69-40

---
Jet cross section ratios
- Determination of αs(MZ) in single-parameter fit
- Test running of αs(Q) (reduced PDF dependence)
- Some reduction in sensitivity
- But cancellation of many systematic effects
- More scale choices

---
Sensitivity vs. systematic effects
Inclusive 3-jet
cross section
Inclusive 3-jet to inclusive 2-jet
cross section ratio
Inclusive 2-jet
cross section
Reduced
sensitivity
Much reduced
systematic uncertainty
\sigma_\text{3j}\propto \alpha_s^3
\sigma_\text{2j}\propto \alpha_s^2
R_{3/2}\propto \alpha_s

---
3- to 2-jet ratios
M. Wobisch
R3/2
2011
αs = 0.124
αs = 0.106
Fits only above 420 GeV
2
NNPDF
CMS: R3/2
- Ratio of inclusive 3- to
  inclusive 2-jet events
- anti-kT R=0.7
- Min. jet pT: 150 GeV
- Max. rap.: |y| < 2.5
- Data 2011 7 TeV,
  and 2012 8 TeV prel.
√s / [TeV]	lum / [fb-1]	αs(MZ)	exp NP PDF	scale
7	5.0	0.1148	23	50
8	19.7	0.1150	22	+50
→ αs

---
Running of αs(Q)
Perform fits in
fixed intervals
of the chosen
scale Q
NLO
Jet cross sections
and ratios
Needs an update for
latest ATLAS, CMS, & H1 points ...
New range explored at LHC
\alpha_s(Q)

---
Running of αs(Q)
Perform fits in
fixed intervals
of the chosen
scale Q
NLO
→ 8 TeV
→ ATLAS
ttbar NNLO
Normalised
distributions
Needs an update for
latest ATLAS, CMS, & H1 points ...
New range explored at LHC
\alpha_s(Q)

---
Normalised distributions
ATLAS:
PLB 750 (2015) 427; EPJC 77 (2017) 872;
PRD98 (2018) 092004.
Relevant ATLAS & CMS measurements:
Proton
Proton
Event shapes

---
Normalised distributions
Pros & cons similar as for cross section ratios ...
- Determination of αs(MZ) in single-parameter fit
- Test running of αs(Q) (reduced PDF dependence)
- Some reduction in sensitivity
- But cancellation of many systematic effects
- More scale choices

---
Transverse energy-energy correlation
2 → 2
2 → 2
2 → n>2
\frac{1}{\sigma}\frac{d\Sigma}{d\cos\phi} = \frac{1}{N}\sum^{N}_{A=1}\sum_{ij}\frac{E^A_{\text{T}i}E^A_{\text{T}j}} {\left(\sum_k{}E^A_{\text{T}k}\right)^2}\delta(\cos\phi-\cos\phi_{ij})
\frac{1}{\sigma}\frac{d\Sigma^\text{asym}}{d\cos\phi} = \frac{1}{\sigma}\frac{d\Sigma}{d\cos\phi}\left|_{\phi} - \frac{1}{\sigma}\frac{d\Sigma}{d\cos\phi}\right|_{\pi-\phi}
\text{TEEC} \propto \alpha_s
\text{ATEEC} \propto \alpha_s

---
(A)TEEC in bins of Q = (pT1+pT2 )/2
Theory:
3-jet NLOJet++
Scale choice:
2011 7 TeV:
μR = μF = (pT1+pT2)/2
2012 8 TeV:
μR = (pT1+pT2)/2
μF = (pT1+pT2)/4
√s / [TeV]	lum / [fb-1]	αs(MZ)	exp NP PDF	scale
7	0.16	0.1173	20	+63-20
8	20.2	0.1162	21	+76-61
7	0.16	0.1195	24	+60-15
8	20.2	0.1196	22	+61-13
Orange: TEEC
Blue: ATEEC

---
Dijet azimuthal decorrelation
Determine αs(Q) from additonal parton branchings separated in Φ around the two leading jets. Binning in sum of scalar transverse momentum HT and rapidity separation y*.
If Δφmax in 3-jet region
Wobisch et al., JHEP 01 (2013) 172;
KR, M. Wobisch, JHEP 12 (2015) 024.
R_{\Delta\phi}(H_T,y^*;\Delta\phi_\mathrm{max}) = \frac {\frac{d^2\sigma_\mathrm{dijet}(\Delta\phi_\mathrm{dijet}<\Delta\phi_\mathrm{max})} {dH_Tdy^*}} {\frac{d^2\sigma_\mathrm{dijet}(\mathrm{inclusive})} {dH_Tdy^*}}
R_{\Delta\phi} \propto \alpha_s

---
RΔΦ in bins of Q = HT/2
Theory:
3-jet NLOJet++
Scale choice: μR = μF = HT/2
From more precise results with
Δφmax = 7π/8 in the two y* regions below 1.0:
√s / [TeV]	lum / [fb-1]	αs(MZ)	exp NP PDF	scale
8	20.2	0.1127	+36-19	+52-19

---
Wrap up & concerns
- Correlations to LHC data already in PDF fits
- Correlations between αs(MZ), Mtop, g(x)
- (Gu)estimation of nonperturbative effects:
  - Different event generators & tunes, different orders, different ...
  - Incoherent among ATLAS, CMS, Tevatron, …
- Conventional scale variation by factors of ½, 2 and 1σ assumption
- Central scale choice …!

---
Scale choices
- Inclusive jets
- Dijets
- 3-jets
- Ratios
- Shapes
- V+jets
\mu_0 = p_\mathrm{T,1}, \quad p_\mathrm{T,jet},\quad \hat{H}_\mathrm{T} ?
\mu_0 = p_\mathrm{T,1}, \quad p_\mathrm{T,1}\cdot\exp\left(0.3y^*\right) ?
\mu_0 = p_\mathrm{T,3},\quad \left( p_\mathrm{T,1}+p_\mathrm{T,2}\right)/2, \quad m_{jjj}/2?
\mu_0 = \sqrt{M_Z^2 + p_\mathrm{TZ}^2} + H_\mathrm{T,jet} ?
\mu_0 = \left( p_\mathrm{T,1}+p_\mathrm{T,2}\right)/2, \quad m_{jj}/2?

---
Perspectives & educated guesses
Experiment:
  - Done: Observables σ ~ αs2, αs3; R3/2 ~ αs; 7 TeV; full phase space
  - Mostly done, 8 TeV data: Some reduction in experimental uncertainty
  - Partially done, 13 TeV: Final precision?
  - Best JEC phase space: Further reduction by some permille?
  - Other observables: Ratios (n+m) / n jets (incl. γ, W, Z), Normalized cross sections (A)TEEC, RΔΦ, RΔR (→ D0)
- Theory:
  - Scales: NNLO important → reduction by 2 – 3 percent!?
  - PDFs: Much improved after LHC I, also HERA 2 data available
    - Better known gluon (Attention circularity jets → g(x) & jets → αs)
    - Fits combining observables at various √s to disentangle g(x), Mt, αs
  - NNLO ratios?
  - NP effects?

---
PDG Summary
PDG2016
LHC data, but not in average
since only NLO theory!
Dominated by
Lattice Gauge Theory
PDG´92: 2.4%
PDG, Chin. Phys. C 40 (2016) 100001.
\frac{\Delta\alpha_S(M_Z)}{\alpha_S(M_Z) } = 0.9\%

---
PDG Summary
PDG2016
LHC data, but not in average
since only NLO theory!
Dominated by
Lattice Gauge Theory
PDG´92: 2.4%
PDG, Chin. Phys. C 40 (2016) 100001.
\frac{\Delta\alpha_S(M_Z)}{\alpha_S(M_Z) } = 0.9\%
To be updated very soon!

---
Summary & Outlook
- LHC at 7 TeV and 8 TeV enables measurements up to scales of 2 TeV
- 13 TeV data yet to be fully evaluated
- Theory at NNLO QCD + electroweak corrections are a must!
- Typical uncertainties on αs(MZ):
  - Experimental: ~ 1 – 2 %
  - PDF: ~ 1 – 2 %
  - Scale: 3 – 5 % → 1 – 2% at NNLO(?) but still an issue. Central scale choice?
  - Nonpert. Effects: 1 % (really?)
Beyond one experiment ( see also → LHC EW Working Group):
  - Combined fits of ATLAS & CMS (LHC) measurements
  - Combined fits of HERA, Tevatron & LHC measurements
CHALLENGE: αs(MZ) at 1% or better from hadron colliders!

---
Thank you for your attention
and the invitation to speak here!

---
Backup Slides

---
Jet energy scale and αS
Two goals for αS:
1. Measure the running of αS(Q) up
    to the highest scales possible
→ In CMS mostly looked into αS(Q)!
2. Measure αS(MZ) as precisely as
    possible
→ For αS(MZ) might want to stay
    at minimal JEC uncertainty:
    200 – 800 GeV, central rapidity
Better in:
JEC uncertainty
PDF uncertainty
Evolution to MZ
Worse in: NP effects
Uncomfortably
growing error
Incredibly
shrinking error

---
αS Projections from Snowmass
Still at LHC:
Only jets probe running αS at highest scales
1% uncertainty at MZ challenging, but not impossible
Need NNLO and improved PDFs (gluon) plus some experimental optimization
Still at LHC:
Only jets probe running αS at highest scales
< 1% uncertainty at MZ challenging ...
Need NNLO and improved PDFs (gluon) plus some experimental optimization
~1%
<1%
<1%
~1%
<0.5%
Snowmass QCD Report, arXiv:1310.5189.